## Slide 1: IoT-Enabled and Head-Gesture-Controlled Autonomous Wheelchair Navigation
Presented by,
Md. Masudur Rahman Rabbi
Roll: 1907113
Protya Roy
Roll: 1907025
Department of Computer Science and Engineering
Khulna University of Engineering & Technology
Supervised by,
Dr. Muhammad Sheikh Sadi
Professor
Department of Computer Science and Engineering
Khulna University of Engineering & Technology
CSE 4000
30.08.2025

## Slide 2: Outlines
Introduction
Objectives
Literature Review
Hardware Components
Methodology
Experimental Analysis
Demonstration
Future Works
Conclusions
References
30.08.2025

## Slide 3: Introduction
Traditional wheelchair controls are difficult for users with severe disabilities.
Head gestures: natural head tilts (F/B/L/R) as commands.
Gyro sensor: detects rotation and orientation to track head movements.
Combines for smooth, hands-free navigation, enhancing independence and accessibility.
30.08.2025

## Slide 4: Objectives
The main objectives are to:
develop a hands-free wheelchair control system using head gestures.
utilize gyro(MPU6050) sensor for precise motion detection.
enable smooth navigation in multiple directions.
improve mobility and independence for physically disabled users.
ensure safety, accessibility, and ease of use.
30.08.2025

## Slide 5: Literature Review
30.08.2025
Author name | Method | Findings | Limitations
Azraai, Mohd. et al. [1] | Gyro + microcontroller | Accurate detection, smooth move | Only tested on healthy users
Rahman, M. M. et al. [2] | Accelerometer + Arduino + sensors | Multi-direction, obstacle safety | High cost, complex hardware
Kumar, A. et al. [3] | MPU6050 + wireless | Wireless, improved independence | Prototype only, no validation
Priyatharshini, R. et al. [4] | Accelerometer + GSM | Health monitoring, alerts | Complex, GSM dependency
Ahmed, F. et al. [5] | Gesture + health monitoring | Mobility + safety + health track | Very complex, heavy compute
Table 1 : Summary of Head-Gesture-Controlled Wheelchair Studies

## Slide 6: Hardware Components
30.08.2025
Wheel Chair
Wheelchair chassis
1602 LCD display
Arduino UNO
24V Li-ion battery
Emergency circuit breaker
DC motor
BTS motor driver
ESP32
DS18B20 temp. sensor
MPU6050 gyro sensor
Fig 1 : Hardware components for wheelchair

## Slide 7: Methodology
Fig 2 : Block Diagram of the Head-Gesture-Controlled Wheelchair Navigation

## Slide 8: Methodology (Cont.)
Wheelchair Movement (Steps)
Step 1: Calibration of MPU6050
Step 2: MPU6050 measures head tilt along X, Y, Z axes
Step 3: Tilt thresholds mapped to commands:
  Forward: X > +20° → move forward
  Backward: X < −20° → move backward
  Right: Y > +20° → left motor forward, right motor backward
  Left: Y < −20° → left motor backward, right motor forward
  Stop: X and Y within ±20° → all motors stop
30.08.2025
Fig 2 : Block Diagram of the Head-Gesture-Controlled Wheelchair Navigation

## Slide 9: Methodology (Cont.)
Wheelchair Movement (Steps)
Step 4: Arduino/ESP32 sends PWM signals to motor driver (BTS7960), controlling speed and direction
Step 5: Continuous loop updates motor commands every 10 ms for smooth, real-time response
Dead Zone: Small tilts (±5°) ignored to avoid unintended movement
30.08.2025
Fig 2 : Block Diagram of the Head-Gesture-Controlled Wheelchair Navigation

## Slide 10: Methodology (Cont.)
IoT Based Body Temperature Monitoring
Dedicated ESP32 collects DS18B20 temperature data independently of wheelchair control.
Data sent via Wi-Fi to MySQL database using insert.php.
User app retrieves real-time or historical temperature via get.php.
30.08.2025
Fig 3 : Block diagram of IoT based body temperature monitoring via cloud(MySQL)

## Slide 11: Methodology (Cont.)
IoT Based Body Temperature Monitoring
Local 1602 LCD displays immediate temperature feedback.
Separation ensures wheelchair navigation remains safe and unaffected.
Provides remote health monitoring and reliable operation for the patient.
30.08.2025
Fig 3 : Block diagram of IoT based body temperature monitoring via cloud(MySQL)

## Slide 12: Experimental Analysis
30.08.2025
Performance Testing
Compared Head Gesture, Joystick, and Voice Control.
Tested in indoor, ramps, outdoor, long-term use, and complex tasks.
Key Findings
Head Gesture: Best in narrow spaces, sharp turns, straight paths.
Joystick: Most stable & versatile, especially in long navigation & zigzag paths.
Voice Control: Works on smooth floors, but unreliable in noisy environments & causes fatigue.

## Slide 13: Experimental Analysis (Cont.)
30.08.2025
Scenario | Head Gesture(HG) | Joystick(JS) | Voice Control(VC) | Verdict
Indoor | Accurate, safe | Stable | Delay issues | HG best
Ramp/Surface | Fast, smooth | Consistent | Needs quiet env. | HG best
Outdoor | Slight tilt issue | Stable | Affected by noise | JS best
Long-term Use | Minor neck strain | No fatigue | Voice fatigue | JS best
Task/Speed | Fast in straight/turns | Best in zigzag paths | Slow | Both HG and JS best
Table 2 : Performance Comparison of Control Methods

## Slide 14: Demonstration
(a) (b) (c)
Fig 4: (a) Full demonstration, (b) Circuit connections, (c) MPU6050 mounted on headband

## Slide 15: Future Works
Integrating obstacle detection and avoidance sensors for safer navigation.
Adding advanced health monitoring(heart rate, fall detection)alongside temperature.
Implementing machine learning for adaptive gesture recognition & smoother control.
Exploring solar-powered or energy-efficient systems for longer operational time.
30.08.2025

## Slide 16: Conclusions
Head gesture-controlled wheelchairs provide hands-free, intuitive mobility.
Gyro sensors enable accurate and responsive navigation.
IoT integration allows real-time health monitoring and cloud data storage.
The system enhances independence, accessibility, and user safety.
Future enhancements can further improve usability, intelligence, and energy efficiency.
30.08.2025

## Slide 17: References
30.08.2025
[1] M. A. Mohd Azraai, S.Z. Yahaya, I. Almanzo Chong, Z.H. Che Soh, Z. Hussain and R. Boudville. “Head gestures based movement control of electric wheelchair for people with tetraplegia”, 2022 IEEE 12th International Conference on Control System, Computing and Engineering (ICCSCE), pages 163–167, 2022.
[2] Prannah Dey, Md.Mehedi Hasan, Srijon Mostofa, and Ariful Islam Rana. “Smart wheelchair integrating head gesture navigation”, 2019 International Conference on Robotics,Electrical and Signal Processing Techniques (ICREST), pages 329–334, 2019.
[3] Shivamma D, Manjula M, S Bhavani Prasad, Nikunj Vihari Konakalla, Eshwar Reddy M, and Mir Khyrun Ali. “Smart wheelchair navigation using gesture-based control and iot”, 2025 International Conference on Intelligent and Innovative Technologies in Computing, Electrical and Electronics (IITCEE), pages 1–4, 2025.
[4] Pravin Kumar Sah, Chandra Harsha, Hemanth Dinesh, Nithin Ratkonda, and Lekshmi Vijayan. “Head gesture controlled wheelchair with integrated health monitoring for paralysis patients”, 2024 8th International Conference on I-SMAC (IoT in Social, Mobile, Analytics and Cloud) (I-SMAC), pages 1204–1210, 2024.
[5] Mrunal Patil, Mansi Subhedar, Yash Kamble, and Omkar Labde. “Intelligent wheelchair design: Integrating gesture recognition, health tracking and fall detection”, 2024 8th International Conference on Computing, Communication, Control and Automation (ICCUBEA), pages 1–6, 2024.

## Slide 18: Thank You